## Slide 1: Braille E-Reader
Samuel Kostousov
Grade 9
2021

## Slide 2: Modern Day Braille Displays
$3,775
Image Credit: Humanware
Brailliant BI 40 Braille Display
Image Credit: Amazon
27 Amazon Kindle Paperwhite E-Readers

## Slide 3: Objectives
Create a Braille Display Technology that will be:
  Cost affordable
  Energy efficient

## Slide 4
Braille Character
(Six-Cells)
Side View (One Cell)
Moving Platform
Rotating Platform
Stepper Motor
N
S
N
S
Braille Cell Raised
Moving Platform
Rotating Platform
Stepper Motor
N
S
S
N
Braille Cell Down
Braille Cell Raised
Braille Cell Down

## Slide 6
2H Microstep Driver
PUL+
PUL-
DIR+
DIR-
ENBL+
ENBL-
DC-
DC+
A+
A-
B+
B-
SW8
SW7
SW6
SW5
SW4
SW3
SW2
SW1
ON
ON
ON
OFF
OFF
ON
ON
ON
A-
B-
A+
B+
+
-
Stepper Motor
Arduino Uno Board
Power Bank
(Giving off 24V)
Power

## Slide 7: Code
#include <Arduino.h>
#define PULSE_PIN 8
#define ENABLE_PIN 10
#define DIRECTION_PIN 9
void setup() {
pinMode(PULSE_PIN,OUTPUT);
pinMode(ENABLE_PIN,OUTPUT);
pinMode(DIRECTION_PIN,OUTPUT);
digitalWrite(ENABLE_PIN,HIGH);
}
void loop() {
digitalWrite(PULSE_PIN,LOW);
delay(10);
digitalWrite(PULSE_PIN,HIGH);
delay(10);
}
Defines the control pins
Includes the Arduino library
Sets the previously defined pins to output pins
Sets the driver to ‘on’ (HIGH)
Moves one step (7.5°) and then repeats

## Slide 8: Problems
Problem: The micro stepper motor was too weak
Solution: I tested out the technology on a stronger & bigger stepper motor
P: The motor driver could not handle the required 24 volts and melted my apparatus (Fig.1)
S: I used a stepper motor driver
P: Instead of rising upwards, the moving platform rotated together with the bottom platform
S: I made grooves in the moving platform to allow it to only go upwards
140 C
22 C
Fig.1
Stepper Motor

## Slide 9: Improvements
If I were to redo this project, I would:
  Order motors from several different suppliers to make sure at least one would suit my needs.
  Minimize the amount of area taken up by the tube surrounding the mechanism.
  Wire the motor straight to the control board.

## Slide 10: Prices
Material | Price
3D printing filament | Approx. $1-$2
12 mini magnets | $0.5
Stepper Motor | $0.75-$4.50
Overall Price of 1 cell: $2.25-$7.00 | 
Overall Price of 1 Braille Character (6 cells): $13.50-$42 | 
My New and Affordable Braille Technology (40 characters, bulk order): $500 - $1680 | 
Brailliant BI 40 Braille Display
VS
My New and Affordable Braille Technology

## Slide 11: Conclusion
Although the price is still high compared to regular e-readers, it’s definitely an improvement from the current e-readers available on the market.
The size isn’t ideal, but this can possibly be improved with the use of smaller stepper motors.
Using smaller stepper motors can also decrease the voltage needed, currently at 24v.

## Slide 12: Extensions & Future Research
Scale down the size
Put together enough cells for at least one character
Lower the energy consumption
Have a blind person test out the technology
Program it to be able to display text files

## Slide 13: Bibliography
Eldridge, A. (2019, Feb 11). Braille. Britannica. www.britannica.com/topic/Braille-writing-system
Eldridge, A. (2021, Jan 02). Louis Braille. Britannica. www.britannica.com/topic/Braille-writing-system
National Federation of the Blind. (2019, January). Blindness Statistics. NFB. www.nfb.org/resources/blindness-statistics
LastMinuteEngineers. (2021). Control Stepper Motor with L298N Motor Driver & Arduino. Last Minute Engineers. https://lastminuteengineers.com/stepper-motor-l298n-arduino-tutorial/
Amazon. (2021). Kindle Paperwhite –Now Waterproof with 2 times the Storage. Amazon. https://www.amazon.ca/All-new-Kindle-Paperwhite-Waterproof-Storage/dp/B07HKYZMQX/ref=sr_1_1?crid=1XCH46ZNYVISJ&dchild=1&keywords=kindle+paperwhite&qid=1615321963&sprefix=kindle+p%2Caps%2C231&sr=8-1
Bridges Canada. (2021). Brailliant BI 40 Braille Display. Bridges Canada. www.bridges-canada.com/products/brailliant-bi-40-braille-display

## Slide 14
Image Credit: BrainPrick
Image Credit: Techaeris
Image Credit: Shutterstock
Notes: Czxdf bmhfgdsa